## Slide 1
Common Motion Planning Framework
Generate the sensor coverage path, then convert it into executable robot motion
COMMON FRAMEWORK / IN DEVELOPMENT
Convert sensor path into robot motion
Select a planning option by use case
IRT JV
MoveIt 2 + Tesseract
Planned for inspection
HPP / LAAS
Constrained planning
Alternative option
1 Find joint positions for each sensor pose
2 Select continuous, collision-free motion
3 Apply scan speed and trajectory timing
Output: joint positions and velocities over time
Generate the
inspection path
CAD / scan data +
inspection requirements
Set coverage passes,
sensor orientation
and surface distance
Open3D +
Open CASCADE
Digital twin
validation
Verify coverage,
sensor pose and
robot trajectory
Revise and recheck
if needed
FANUC robot execution
After validation and approval
ROS 2 + robot-specific interface
FANUC R-2000iC/210L
Representative CAD and simulation images; actual project environment may differ. Sources: Autodesk Community and FANUC.
Benchmarking completed
HPP and IRT JV approaches compared
for motion planning and execution.
Reuse across use cases and robot brands
Common components and interfaces, with robot-specific adapters.
Choose the planner without rebuilding the complete stack.
Notes: Inspection motion generation: The path-generation component uses panel CAD or measured geometry and inspection requirements to define coverage passes. Each sensor pose includes position, orientation and required stand-off distance from the surface. The motion-planning component uses the robot model to find joint configurations for the sensor poses (inverse kinematics), select a continuous collision-free sequence, and add timing under inspection-speed and robot-motion constraints. The result is a trajectory of joint positions and velocities over time, which can be checked in the digital twin before execution. Infeasible paths require revision. These are intended responsibilities, not a claim that every step has been delivered. Representative imagery: CAD surface with inspection points from Autodesk Community, https://forums.autodesk.com/t5/fusion-manufacture-forum/surface-inspection-exact-points/td-p/10132375 (image https://forums.autodesk.com/t5/image/serverpage/image-id/889442iA7227BE8053AC087/image-size/large?px=999&v=v2). This represents CAD geometry and inspection positions, not the exact continuous scan path of this demonstrator or an Open3D/Open CASCADE screenshot. Digital twin illustration is a FANUC ROBOGUIDE screenshot from https://www.fanucamerica.com/press-releases/fanuc-introduces-enhanced-next-gen-roboguide-robot-simulation-software (image https://cdn.craft.cloud/6166486b-1eb4-43d5-990c-ea573de4e750/assets/images/roboguide-new-features.jpg). It illustrates virtual robot simulation only; ROBOGUIDE is not asserted to be the selected digital twin software. Purpose: board-level explanation of a common motion planning framework under development. Multiple options are intended within one platform and are selected by use case, not run sequentially. IRT JV is planned for this aircraft-panel inspection demonstrator. HPP/LAAS is shown as an alternative framework option, not as already integrated. A completed benchmarking study compared HPP and IRT JV; this slide does not claim a measured winner. Shared trajectory output feeds pre-execution digital twin validation, then robot-specific execution interfaces. If checks fail, revise motion and validate again. Robot-agnostic reuse is a design objective and still requires robot models, drivers and adapters. Sources: user requirements in the current conversation; IRT_JV_vs_LAAS_HPP_Conversation_QA.docx, Library ID libfile_784d5dbdeadc81918f2f567b5e8e5956, pages 3–6. That conversation record describes IRT MoveIt2/Tesseract and ROS2 execution, and LAAS HPP. Scan-path generation from CAD/point clouds can use Open3D/Open CASCADE before robot motion planning. Within the IRT pipeline, Descartes and TrajOpt are described for Cartesian path planning and optimization. Confirm exact vendor integration before presenting those details as delivered. FANUC photograph/product image source: https://www.fanucamerica.com/products/robot/r-2000ic-210l ; image asset https://cdn.craft.cloud/6166486b-1eb4-43d5-990c-ea573de4e750/assets/products/r-2000ic-210l/R-2000iC_210L-Beauty-Shot-Right.png . The image represents the robot model and is not a photograph of the inspection demonstrator. No AI-generated robot imagery is used.