## Slide 1
Motion generation in robotics
Existing framework capabilities connected through configurable, tested interfaces
Tool path
TCP poses on the part
Pattern, area and swathe
Robot path
Joint path q(s)
IK, constraints and collisions
Robot trajectory
Timed motion q(t)
Speed, acceleration and jerk
Execution
Track and adapt
Feedback and replanning
Project foundations
REACT
HPP experience
Perception, constrained planning
and task supervision
Primer-skin NDT inspection
Automatic robot motion
Process constraints and
inspection coverage
Intelligent scan plan
Configurable scanning
Defect visit sequencing
and targeted rescanning
Reuse framework capabilities through stepwise integration
Select HPP, MoveIt2 or Tesseract for each application and integrate its supported capabilities.
Build adapters, configuration and validation evidence. Develop algorithms only for confirmed gaps.
Goal: less manual programming, configurable process paths and reusable planning across robots.
1
Notes: Sources and context: user discussion and milestone specification, 9 October 2026. Project-specific status reflects user descriptions, not an independent maturity assessment. Toolpath generation defines a desired TCP path relative to the workpiece. Robot path generation resolves inverse kinematics, constraints, reachability and collision avoidance. Trajectory generation adds time and dynamic limits. Execution feeds actual state back to control and supervision. q(s) denotes robot configuration along a geometric path, and q(t) is configuration as a function of time. Route/task optimization orders the visits and may call motion planning repeatedly. These layers interact and do not have to be implemented by one library. The three project foundations identify relevant experience and work, not three fully released products. The broader team roadmap retains both conventional planning and a parallel research track for uncertain manipulation.
Integration principle: these stages are acceptance checkpoints for existing framework or project capabilities, not eight algorithm-development work packages. Inventory the exact backend/version first. Reuse supported functions, build adapters and common contracts, verify against native outputs, then run an end-to-end regression. Keep unsupported capabilities explicit and retain backend-specific configuration where a common abstraction would lose required semantics. Implement new algorithms only for demonstrated gaps. Start with a thin end-to-end application where existing assets permit, then extend capabilities in the numbered sequence; do not defer all integration testing to Q4. Dates remain proposed and depend on the capability inventory.

## Slide 2
Integration stages 1–4: data, tool paths and motion
Each stage reuses available implementations, adds an interface and verifies the integrated result
Integration stage | Capability to reuse and integration work | Integration acceptance
1 Data adapters | Reuse framework importers for robot, panel, tool and scene data. Map common frames / units to URDF, CAD / point clouds, MJCF and USD. | Equivalent geometry, joints, limits and frames in selected tools
2 Toolpath interface | Wrap IRT Open CASCADE / point-cloud and HPP-project GMM options. Expose a common configuration for pattern, size, area and swathe. Map supported parameters and return a common TCP toolpath. | Configurable coverage / tool path meets process requirements
3 Planner adapters | Connect HPP / MoveIt2 / Tesseract through a capability-based API. Expose supported PRM / RRT, graph search and Cartesian options. Map Pilz PTP / LIN / CIRC and supported spline orders by backend. Keep RMPflow / cuRobo as candidate dynamic extensions. | Feasible motion plus documented capabilities, limits and failures
4 Validation interface | Reuse backend collision / kinematic checks and add process checks. Normalize clearance, singularity, planning-time and coverage results. Retain Gepetto, Tesseract viewers and RViz for inspection. | Path and process checks pass before sequence optimization
Task supervision
BT / state machine handles state changes and retries. HPP dynamic-BT integration is a planned option.
Capability support varies by backend and version. GMM and HPP dynamic-BT items follow project-specific descriptions.
2
Notes: Sources and context: user discussion and milestone specification, 9 October 2026. Project-specific status reflects user descriptions, not an independent maturity assessment. Milestones follow the exact order requested by the user. M1: retain one canonical semantic data contract and write import/export adapters, rather than assuming URDF, MJCF and USD preserve identical physics. Check coordinate conventions, units, inertias, collision geometry, joints and limits after conversion. MuJoCo uses MJCF natively and supports URDF; Isaac Sim uses OpenUSD assets. M2: the IRT Open CASCADE / point-cloud approach and HPP Gaussian-mixture-model approach are user-reported project implementations, not blanket upstream-library claims. Toolpath configuration should include pattern, region boundary, size, swathe, overlap, direction, stand-off and orientation where required. M3: PRM is itself sampling-based; RRT is another sampling family. Grid/graph search is a candidate capability where suitable, not a capability guaranteed in every framework. LIN, CIRC and polynomial splines need backend-specific mapping and continuity checks. Expose only supported spline orders. Pilz supports PTP/LIN/CIRC; MoveIt Cartesian waypoint interpolation is a separate option. RMPflow is a reactive local motion policy and cuRobo offers motion generation, trajectory optimization and MPC APIs; neither label guarantees end-to-end hard real-time execution. For a mobile base, evaluate DWA/DWB in the navigation stack if that was intended by DWM; it is not a generic arm-planning default. BT/state-machine supervision belongs to task orchestration, not necessarily inside a planner. HPP dynamic behavior-tree availability remains a project dependency. M4: viewers display results, while collision, kinematics and coverage-checking components produce the evidence. Sources: https://moveit.picknik.ai/main/doc/how_to_guides/pilz_industrial_motion_planner/pilz_industrial_motion_planner.html ; https://mujoco.readthedocs.io/en/stable/modeling.html ; https://docs.isaacsim.omniverse.nvidia.com/latest/openusd_tuning_tutorials/tutorial_01_asset_structure.html ; https://curobo.org/get_started/7_api.html ; https://docs.isaacsim.omniverse.nvidia.com/6.0.1/manipulators/motion_generation_overview.html . The current Isaac documentation marks the legacy motion-generation API deprecated, so pin and review the selected version when integrating RMPflow.
Integration principle: these stages are acceptance checkpoints for existing framework or project capabilities, not eight algorithm-development work packages. Inventory the exact backend/version first. Reuse supported functions, build adapters and common contracts, verify against native outputs, then run an end-to-end regression. Keep unsupported capabilities explicit and retain backend-specific configuration where a common abstraction would lose required semantics. Implement new algorithms only for demonstrated gaps. Start with a thin end-to-end application where existing assets permit, then extend capabilities in the numbered sequence; do not defer all integration testing to Q4. Dates remain proposed and depend on the capability inventory.

## Slide 3
Integration stages 5–8: optimization to execution
Connect the existing optimization and execution capabilities to the common pipeline
Integration stage | Capability to reuse and integration work | Integration acceptance
5 Sequencing adapter | Wrap existing TSP / GTSP project implementations. Map feasible transition costs, visit groups and optimized task order. | Feasible task order with reduced travel / cycle-time cost
6 Optimization adapter | Expose backend smoothing, blending and time-parameterization. Normalize limits / objectives and revalidate the modified trajectory. | Continuous timed trajectory with all constraints rechecked
7 Simulation adapters | Connect a selected simulator and controller interface first. Extend to Isaac Sim / MuJoCo / Genesis and virtual controllers such as ROBOGUIDE through supported RXU connections. | Collision / dynamics / tracking and controller-handoff evidence
8 Execution adapters | Connect rxu.connectivity ROS / vendor protocol adapters. Map trajectory commands and state feedback to RXU control. Verify buffering, cancellation, stop and recovery on the robot. | Controlled robot trials, process quality and recovery evidence
RXU path planner integration
Common request / trajectory / status contract. MoveIt2 remains in a ROS2 runtime behind an adapter.
The adapter maps scene updates, cancellation and feedback to RXU control / connectivity.
Simulation supports validation. Physical commissioning and the cell safety system remain necessary.
3
Notes: Sources and context: user discussion and milestone specification, 9 October 2026. Project-specific status reflects user descriptions, not an independent maturity assessment. M5 preserves the user-requested sequencing after initial path validation. Build a cost matrix from feasible motion transitions, optimize order and then regenerate/revalidate changed transitions; sequencing and motion may iterate. TSP/GTSP are route/task optimizers. HPP availability refers to project integration, not a claim that every HPP installation includes them. Investigate reuse in other frameworks rather than assume availability. M6 reruns collision, process and joint-limit checks after smoothing, blending or retiming. Smooth geometry does not imply smooth timing. M7 uses simulator adapters for robot model loading, timed command playback and measured state. Virtual controllers expose different supported protocols and licensing; confirm ROBOGUIDE or other vendor-controller connectivity before committing. Simulation cannot establish complete safety; use commissioning, risk assessment and independent cell safety functions. M8 protocol adapters must support correct units, modes, timestamp semantics, buffering, cancellation and stop acknowledgement. Preserve rail/arm exclusivity for the NDT cell where required. The principal MoveIt2 integration challenge is isolating ROS2 dependency. Proposed solution: a separate ROS2 component/process behind a stable RXU service boundary, mapping canonical requests to MoveIt messages and results back to a common trajectory contract. This isolates dependency without claiming to remove ROS2 from MoveIt2. Versioned robot and scene snapshots, timeout/error codes and execution feedback belong to this contract. Sources: https://moveit.picknik.ai/main/doc/concepts/hybrid_planning/hybrid_planning.html ; https://github.com/tesseract-robotics/tesseract_planning . Simulation and connectivity entries are proposed integration targets, not claims that every protocol currently works.
Integration principle: these stages are acceptance checkpoints for existing framework or project capabilities, not eight algorithm-development work packages. Inventory the exact backend/version first. Reuse supported functions, build adapters and common contracts, verify against native outputs, then run an end-to-end regression. Keep unsupported capabilities explicit and retain backend-specific configuration where a common abstraction would lose required semantics. Implement new algorithms only for demonstrated gaps. Start with a thin end-to-end application where existing assets permit, then extend capabilities in the numbered sequence; do not defer all integration testing to Q4. Dates remain proposed and depend on the capability inventory.

## Slide 4
Stepwise framework integration roadmap
2027 integrates and verifies existing capabilities. Later R&T extends the supported operating conditions.
Q1 2027
M1 Connect data adapters
M2 Wrap toolpath options
Gate: toolpath through common API
Q2 2027
M3 Integrate planner APIs
M4 Unify path checks
Gate: validated planner output
Q3 2027
M5 Connect sequencing
M6 Expose optimization
Gate: optimized output revalidated
Q4 2027
M7 Connect simulation
M8 Connect robot execution
Gate: simulation-to-robot evidence
2027 supporting work
Start with one application / backend, then add alternatives through the same contracts.
RXU / ROS2 adapters, BT supervision and regression tests support every integration stage.
2028
Dynamic adaptation
Scene-driven replanning, local correction and process-aware recovery.
Evaluate RMPflow / cuRobo and planned HPP dynamic-BT integration.
2029+
Learning under uncertainty
Cloth / deformables and varied-object grasping:
compare VLA / imitation learning and RL with conventional baselines.
Proposed dates depend on resources and robot access. 2028 expansion targets potential LuFo funding. Learning data preparation starts in 2027.
4
Notes: Sources and context: user discussion and milestone specification, 9 October 2026. Project-specific status reflects user descriptions, not an independent maturity assessment. This is a proposed planning sequence, not a funded delivery promise. Q1: establish model/data contracts and coverage configuration. Q2: integrate and compare a primary backend and a justified second backend, preserving the architecture for HPP, MoveIt2 and Tesseract. Q3: sequence tasks and optimize timing/paths with revalidation. Q4: validate a selected simulator/controller route, then demonstrate on the physical robot. Every framework, simulator and vendor protocol need not be production-ready in 2027; prioritize reference implementations and versioned adapter contracts. RXU integration is one cross-cutting workstream, not the overall roadmap. 2028: use the potential LuFo boost for event-driven replanning, bounded online correction and process-aware recovery. Dynamic BT supervision is a proposed project option, subject to availability. For learning, start task selection, conventional baselines and data collection in 2027; run a bounded pilot if funding permits in 2028; evaluate transfer to unseen cloth configurations, deformable materials and varied objects in 2029+. VLA refers to a vision-language-action policy; RL is a training method, and they can be combined. Uncertainty alone does not prove learning will outperform conventional methods. Compare completion rate, generalization, interventions, recovery, latency and process accuracy. Across all phases measure planning time, TCP error, coverage, continuity and manual programming effort; set numerical thresholds with the application owners. Sources: https://www.physicalintelligence.company/blog/pi0 ; https://curobo.org/ ; https://research.nvidia.com/publication/2020-11_rmpflow-geometric-framework-generation-multi-task-motion-policies .
Integration principle: these stages are acceptance checkpoints for existing framework or project capabilities, not eight algorithm-development work packages. Inventory the exact backend/version first. Reuse supported functions, build adapters and common contracts, verify against native outputs, then run an end-to-end regression. Keep unsupported capabilities explicit and retain backend-specific configuration where a common abstraction would lose required semantics. Implement new algorithms only for demonstrated gaps. Start with a thin end-to-end application where existing assets permit, then extend capabilities in the numbered sequence; do not defer all integration testing to Q4. Dates remain proposed and depend on the capability inventory.