## Slide 1
Motion generation in robotics
Existing framework capabilities connected through configurable, tested interfaces
Tool path
TCP poses on the part
Pattern, area and swathe
Robot path
Joint path q(s)
IK, constraints and collisions
Robot trajectory
Timed motion q(t)
Speed, acceleration and jerk
Execution
Track and adapt
Feedback and replanning
Project foundations
REACT
HPP experience
Perception, constrained planning
and task supervision
Primer-skin NDT inspection
Automatic robot motion
Process constraints and
inspection coverage
Intelligent scan plan
Configurable scanning
Defect visit sequencing
and targeted rescanning
Framework capability and use case benchmarks
Compare HPP, MoveIt2, Tesseract and Drake; qualify planner choices per process.
Reuse proven capabilities through common interfaces, staged validation and RXU connectivity.
Goal: less manual programming, configurable process paths and reusable planning across robots.
1
Notes: Sources and context: user discussion and milestone specification, 9 October 2026. Project-specific status reflects user descriptions, not an independent maturity assessment. Toolpath generation defines a desired TCP path relative to the workpiece. Robot path generation resolves inverse kinematics, constraints, reachability and collision avoidance. Trajectory generation adds time and dynamic limits. Execution feeds actual state back to control and supervision. q(s) denotes robot configuration along a geometric path, and q(t) is configuration as a function of time. Route/task optimization orders the visits and may call motion planning repeatedly. These layers interact and do not have to be implemented by one library. The three project foundations identify relevant experience and work, not three fully released products. The broader team roadmap retains both conventional planning and a parallel research track for uncertain manipulation.
Integration principle: these stages are acceptance checkpoints for existing framework or project capabilities, not eight algorithm-development work packages. Inventory the exact backend/version first. Reuse supported functions, build adapters and common contracts, verify against native outputs, then run an end-to-end regression. Keep unsupported capabilities explicit and retain backend-specific configuration where a common abstraction would lose required semantics. Implement new algorithms only for demonstrated gaps. Start with a thin end-to-end application where existing assets permit, then extend capabilities in the numbered sequence; do not defer all integration testing to Q4. Dates remain proposed and depend on the capability inventory.
Benchmark qualification: use the same robot, tool, workpiece, scene, constraints and hardware budget across candidates. Report median and tail latency, planning success, clearance, continuity, coverage, process quality, cycle time and recovery performance over repeated trials. Separate native capabilities, external integrations, project extensions and measured results. Do not imply all frameworks implement every planner.
HPP: use the current Python binding approach (hpp-python / pyhpp), not a blanket CORBA dependency. Treat GMM toolpaths, dynamic behavior trees and memory-based path reuse as project/release-specific capabilities until the exact build and API are demonstrated. Revalidate cached paths after robot, tool, scene or process changes.
Two benchmark levels: compare framework capability and RXU integration effort; then qualify planner / pipeline choices for each use case. Include maintenance, licensing, deployment, determinism, compute cost and support. See Airbus_Robotics_Complete_Benchmark_Study.docx for the detailed criteria and evidence register.
2027 is a staged integration target, subject to resources, not a commitment to every framework, simulator and robot protocol. Establish one thin end-to-end flow early, benchmark continuously, and expand by qualification gates. Simulation supports validation but does not establish physical robot safety; cell risk assessment, controller safeguards and controlled commissioning remain required.

## Slide 2
Integration stages 1–4: data, tool paths and motion
Each stage reuses available implementations, adds an interface and verifies the integrated result
Integration stage | Capability to reuse and integration work | Integration acceptance
M1 Data interfaces | Common robot, tool and panel model: frames, units, joints, limits, CAD and point clouds. Convert URDF / MJCF / USD as needed. | Geometry, calibration and model uncertainty checked.
M2 Toolpath interface | Wrap IRT CAD / point-cloud and project GMM approaches. Configure pattern, area, size, swathe, overlap, tool orientation and standoff. | Coverage, reachability and process constraints met.
M3 Planner adapters | Common API for HPP, MoveIt2, Tesseract and Drake. Qualify sampling, graph, Cartesian and optimization options; evaluate reactive backends separately. | Feasible motion; latency, limits and RXU effort recorded.
M4 Initial validation | Collision, clearance, IK / posture continuity, singularity and process checks. Record generation time and coverage; inspect with suitable viewers. | Repeatable path checks before sequencing.
Task supervision
BT / state-machine orchestration across stages: monitor scene and execution state, handle failures and log decisions.
Capability support varies by backend and version. GMM and HPP dynamic-BT items follow project-specific descriptions.
2
Notes: Sources and context: user discussion and milestone specification, 9 October 2026. Project-specific status reflects user descriptions, not an independent maturity assessment. Milestones follow the exact order requested by the user. M1: retain one canonical semantic data contract and write import/export adapters, rather than assuming URDF, MJCF and USD preserve identical physics. Check coordinate conventions, units, inertias, collision geometry, joints and limits after conversion. MuJoCo uses MJCF natively and supports URDF; Isaac Sim uses OpenUSD assets. M2: the IRT Open CASCADE / point-cloud approach and HPP Gaussian-mixture-model approach are user-reported project implementations, not blanket upstream-library claims. Toolpath configuration should include pattern, region boundary, size, swathe, overlap, direction, stand-off and orientation where required. M3: PRM is itself sampling-based; RRT is another sampling family. Grid/graph search is a candidate capability where suitable, not a capability guaranteed in every framework. LIN, CIRC and polynomial splines need backend-specific mapping and continuity checks. Expose only supported spline orders. Pilz supports PTP/LIN/CIRC; MoveIt Cartesian waypoint interpolation is a separate option. RMPflow is a reactive local motion policy and cuRobo offers motion generation, trajectory optimization and MPC APIs; neither label guarantees end-to-end hard real-time execution. For a mobile base, evaluate DWA/DWB in the navigation stack if that was intended by DWM; it is not a generic arm-planning default. BT/state-machine supervision belongs to task orchestration, not necessarily inside a planner. HPP dynamic behavior-tree availability remains a project dependency. M4: viewers display results, while collision, kinematics and coverage-checking components produce the evidence. Sources: https://moveit.picknik.ai/main/doc/how_to_guides/pilz_industrial_motion_planner/pilz_industrial_motion_planner.html ; https://mujoco.readthedocs.io/en/stable/modeling.html ; https://docs.isaacsim.omniverse.nvidia.com/latest/openusd_tuning_tutorials/tutorial_01_asset_structure.html ; https://curobo.org/get_started/7_api.html ; https://docs.isaacsim.omniverse.nvidia.com/6.0.1/manipulators/motion_generation_overview.html . The current Isaac documentation marks the legacy motion-generation API deprecated, so pin and review the selected version when integrating RMPflow.
Integration principle: these stages are acceptance checkpoints for existing framework or project capabilities, not eight algorithm-development work packages. Inventory the exact backend/version first. Reuse supported functions, build adapters and common contracts, verify against native outputs, then run an end-to-end regression. Keep unsupported capabilities explicit and retain backend-specific configuration where a common abstraction would lose required semantics. Implement new algorithms only for demonstrated gaps. Start with a thin end-to-end application where existing assets permit, then extend capabilities in the numbered sequence; do not defer all integration testing to Q4. Dates remain proposed and depend on the capability inventory.
Benchmark qualification: use the same robot, tool, workpiece, scene, constraints and hardware budget across candidates. Report median and tail latency, planning success, clearance, continuity, coverage, process quality, cycle time and recovery performance over repeated trials. Separate native capabilities, external integrations, project extensions and measured results. Do not imply all frameworks implement every planner.
HPP: use the current Python binding approach (hpp-python / pyhpp), not a blanket CORBA dependency. Treat GMM toolpaths, dynamic behavior trees and memory-based path reuse as project/release-specific capabilities until the exact build and API are demonstrated. Revalidate cached paths after robot, tool, scene or process changes.
Two benchmark levels: compare framework capability and RXU integration effort; then qualify planner / pipeline choices for each use case. Include maintenance, licensing, deployment, determinism, compute cost and support. See Airbus_Robotics_Complete_Benchmark_Study.docx for the detailed criteria and evidence register.
2027 is a staged integration target, subject to resources, not a commitment to every framework, simulator and robot protocol. Establish one thin end-to-end flow early, benchmark continuously, and expand by qualification gates. Simulation supports validation but does not establish physical robot safety; cell risk assessment, controller safeguards and controlled commissioning remain required.

## Slide 3
Integration stages 5–8: optimization to execution
Connect the existing optimization and execution capabilities to the common pipeline
Integration stage | Capability to reuse and integration work | Integration acceptance
M5 Task / route order | TSP / GTSP or scheduling adapters. Include robot travel cost, process precedence, tool changes and shared resources. | Feasible order; cycle-time benefit vs baseline.
M6 Path / trajectory | Optimize geometry and timing under joint, process and smoothness limits. Reuse cached paths only after scene / model / tool revalidation. | Limits, continuity and quality preserved.
M7 Simulation validation | Connect selected physics simulator and vendor virtual controller via RXU. Check timing, tracking, I/O and process behavior. | Execution fidelity checked; simulation is not safety proof.
M8 RXU execution | Map trajectories to robot protocols and controller limits. Monitor feedback, buffering and tracking; verify stop / resume and recovery. | Controlled cell trials and acceptance gates passed.
RXU path planner integration
RXU owns connectivity and execution feedback. Planner adapters share contracts; simulator and controller support are qualified per robot / process.
Simulation supports validation. Physical commissioning and the cell safety system remain necessary.
3
Notes: Sources and context: user discussion and milestone specification, 9 October 2026. Project-specific status reflects user descriptions, not an independent maturity assessment. M5 preserves the user-requested sequencing after initial path validation. Build a cost matrix from feasible motion transitions, optimize order and then regenerate/revalidate changed transitions; sequencing and motion may iterate. TSP/GTSP are route/task optimizers. HPP availability refers to project integration, not a claim that every HPP installation includes them. Investigate reuse in other frameworks rather than assume availability. M6 reruns collision, process and joint-limit checks after smoothing, blending or retiming. Smooth geometry does not imply smooth timing. M7 uses simulator adapters for robot model loading, timed command playback and measured state. Virtual controllers expose different supported protocols and licensing; confirm ROBOGUIDE or other vendor-controller connectivity before committing. Simulation cannot establish complete safety; use commissioning, risk assessment and independent cell safety functions. M8 protocol adapters must support correct units, modes, timestamp semantics, buffering, cancellation and stop acknowledgement. Preserve rail/arm exclusivity for the NDT cell where required. The principal MoveIt2 integration challenge is isolating ROS2 dependency. Proposed solution: a separate ROS2 component/process behind a stable RXU service boundary, mapping canonical requests to MoveIt messages and results back to a common trajectory contract. This isolates dependency without claiming to remove ROS2 from MoveIt2. Versioned robot and scene snapshots, timeout/error codes and execution feedback belong to this contract. Sources: https://moveit.picknik.ai/main/doc/concepts/hybrid_planning/hybrid_planning.html ; https://github.com/tesseract-robotics/tesseract_planning . Simulation and connectivity entries are proposed integration targets, not claims that every protocol currently works.
Integration principle: these stages are acceptance checkpoints for existing framework or project capabilities, not eight algorithm-development work packages. Inventory the exact backend/version first. Reuse supported functions, build adapters and common contracts, verify against native outputs, then run an end-to-end regression. Keep unsupported capabilities explicit and retain backend-specific configuration where a common abstraction would lose required semantics. Implement new algorithms only for demonstrated gaps. Start with a thin end-to-end application where existing assets permit, then extend capabilities in the numbered sequence; do not defer all integration testing to Q4. Dates remain proposed and depend on the capability inventory.
Benchmark qualification: use the same robot, tool, workpiece, scene, constraints and hardware budget across candidates. Report median and tail latency, planning success, clearance, continuity, coverage, process quality, cycle time and recovery performance over repeated trials. Separate native capabilities, external integrations, project extensions and measured results. Do not imply all frameworks implement every planner.
HPP: use the current Python binding approach (hpp-python / pyhpp), not a blanket CORBA dependency. Treat GMM toolpaths, dynamic behavior trees and memory-based path reuse as project/release-specific capabilities until the exact build and API are demonstrated. Revalidate cached paths after robot, tool, scene or process changes.
Two benchmark levels: compare framework capability and RXU integration effort; then qualify planner / pipeline choices for each use case. Include maintenance, licensing, deployment, determinism, compute cost and support. See Airbus_Robotics_Complete_Benchmark_Study.docx for the detailed criteria and evidence register.
2027 is a staged integration target, subject to resources, not a commitment to every framework, simulator and robot protocol. Establish one thin end-to-end flow early, benchmark continuously, and expand by qualification gates. Simulation supports validation but does not establish physical robot safety; cell risk assessment, controller safeguards and controlled commissioning remain required.

## Slide 4
Stepwise framework integration roadmap
2027 integrates and verifies existing capabilities. Later R&T extends the supported operating conditions.
Q1 2027
M1 Connect data adapters
M2 Wrap toolpath options
Gate: toolpath through common API
Q2 2027
M3 Integrate planner APIs
M4 Unify path checks
Gate: validated planner output
Q3 2027
M5 Connect sequencing
M6 Expose optimization
Gate: optimized output revalidated
Q4 2027
M7 Connect simulation
M8 Connect robot execution
Gate: simulation-to-robot evidence
Continuous qualification
Benchmark at every stage; deliver one thin end-to-end use case early.
Build RXU adapters, regression tests, orchestration and learning-data logs.
2028
Dynamic adaptation
Replanning, moving obstacles, local correction and contact-control integration.
Validate recovery and path reuse; evaluate RMPflow, cuRobo and HPP dynamic BT.
2029+
Learning under uncertainty
Cloth / deformables and varied-object grasping:
compare VLA / imitation learning and RL with conventional baselines.
Proposed dates depend on resources and robot access. 2028 expansion targets potential LuFo funding. Learning data preparation starts in 2027.
4
Notes: Sources and context: user discussion and milestone specification, 9 October 2026. Project-specific status reflects user descriptions, not an independent maturity assessment. This is a proposed planning sequence, not a funded delivery promise. Q1: establish model/data contracts and coverage configuration. Q2: integrate and compare a primary backend and a justified second backend, preserving the architecture for HPP, MoveIt2 and Tesseract. Q3: sequence tasks and optimize timing/paths with revalidation. Q4: validate a selected simulator/controller route, then demonstrate on the physical robot. Every framework, simulator and vendor protocol need not be production-ready in 2027; prioritize reference implementations and versioned adapter contracts. RXU integration is one cross-cutting workstream, not the overall roadmap. 2028: use the potential LuFo boost for event-driven replanning, bounded online correction and process-aware recovery. Dynamic BT supervision is a proposed project option, subject to availability. For learning, start task selection, conventional baselines and data collection in 2027; run a bounded pilot if funding permits in 2028; evaluate transfer to unseen cloth configurations, deformable materials and varied objects in 2029+. VLA refers to a vision-language-action policy; RL is a training method, and they can be combined. Uncertainty alone does not prove learning will outperform conventional methods. Compare completion rate, generalization, interventions, recovery, latency and process accuracy. Across all phases measure planning time, TCP error, coverage, continuity and manual programming effort; set numerical thresholds with the application owners. Sources: https://www.physicalintelligence.company/blog/pi0 ; https://curobo.org/ ; https://research.nvidia.com/publication/2020-11_rmpflow-geometric-framework-generation-multi-task-motion-policies .
Integration principle: these stages are acceptance checkpoints for existing framework or project capabilities, not eight algorithm-development work packages. Inventory the exact backend/version first. Reuse supported functions, build adapters and common contracts, verify against native outputs, then run an end-to-end regression. Keep unsupported capabilities explicit and retain backend-specific configuration where a common abstraction would lose required semantics. Implement new algorithms only for demonstrated gaps. Start with a thin end-to-end application where existing assets permit, then extend capabilities in the numbered sequence; do not defer all integration testing to Q4. Dates remain proposed and depend on the capability inventory.
Benchmark qualification: use the same robot, tool, workpiece, scene, constraints and hardware budget across candidates. Report median and tail latency, planning success, clearance, continuity, coverage, process quality, cycle time and recovery performance over repeated trials. Separate native capabilities, external integrations, project extensions and measured results. Do not imply all frameworks implement every planner.
HPP: use the current Python binding approach (hpp-python / pyhpp), not a blanket CORBA dependency. Treat GMM toolpaths, dynamic behavior trees and memory-based path reuse as project/release-specific capabilities until the exact build and API are demonstrated. Revalidate cached paths after robot, tool, scene or process changes.
Two benchmark levels: compare framework capability and RXU integration effort; then qualify planner / pipeline choices for each use case. Include maintenance, licensing, deployment, determinism, compute cost and support. See Airbus_Robotics_Complete_Benchmark_Study.docx for the detailed criteria and evidence register.
2027 is a staged integration target, subject to resources, not a commitment to every framework, simulator and robot protocol. Establish one thin end-to-end flow early, benchmark continuously, and expand by qualification gates. Simulation supports validation but does not establish physical robot safety; cell risk assessment, controller safeguards and controlled commissioning remain required.

## Slide 5
Use case qualification and success measures
Proposed demonstrators establish evidence before expanding to further process families.
Use case | Proposed demonstration | Evidence of success
Curved-panel inspection | Configurable coverage with swathe, overlap, sensor orientation and standoff; compare planner choices on the same panel. | Coverage, image quality, clearance and cycle time.
Targeted defect inspection | 100+ inspection targets; compare TSP / GTSP ordering with robot-feasible transitions and posture choices. | Visit completeness, route cost and planning time.
Drilling + cleaning | Enforce clean / drill / post-clean sequence, tool changes, approach / retract and interruption recovery. | Hole quality, sequence compliance and safe resume.
Next process families | Assembly, auto rigging, painting, sanding, logistics, pick-and-place, masking and resin deposition; qualify process-specific constraints. | Contact / force, finish, accuracy and resource use.
Measure value against the current OLP workflow
Track preparation and changeover hours, physical trials, reusable paths and operator effort, alongside process quality, cycle time and recovery success.
Common datasets, baselines and acceptance thresholds; framework selection remains evidence-led.
5
Notes: The first three demonstrators are proposals and require dataset, robot, process-owner and resource agreement. Freeze quantitative acceptance thresholds with stakeholders before trials. Curved-panel inspection validates configurable coverage; targeted inspection tests ordering and posture choices; drilling with cleaning tests process precedence, tool I/O and recovery. Subsequent qualification includes assembly, auto rigging, painting, sanding, drilling, logistics, pick and place, cleaning, masking and resin deposition. No universal best planner is asserted. Select candidates by the measured use-case requirements and maintain a fallback execution strategy. For contact processes, qualify the force-control loop and its integration independently from geometric planning.
Benchmark qualification: use the same robot, tool, workpiece, scene, constraints and hardware budget across candidates. Report median and tail latency, planning success, clearance, continuity, coverage, process quality, cycle time and recovery performance over repeated trials. Separate native capabilities, external integrations, project extensions and measured results. Do not imply all frameworks implement every planner.
HPP: use the current Python binding approach (hpp-python / pyhpp), not a blanket CORBA dependency. Treat GMM toolpaths, dynamic behavior trees and memory-based path reuse as project/release-specific capabilities until the exact build and API are demonstrated. Revalidate cached paths after robot, tool, scene or process changes.
Two benchmark levels: compare framework capability and RXU integration effort; then qualify planner / pipeline choices for each use case. Include maintenance, licensing, deployment, determinism, compute cost and support. See Airbus_Robotics_Complete_Benchmark_Study.docx for the detailed criteria and evidence register.
2027 is a staged integration target, subject to resources, not a commitment to every framework, simulator and robot protocol. Establish one thin end-to-end flow early, benchmark continuously, and expand by qualification gates. Simulation supports validation but does not establish physical robot safety; cell risk assessment, controller safeguards and controlled commissioning remain required.