## Slide 1
Where autonomous motion adds value
The more the part varies, the more autonomy helps
Same part, every time
Many variants: plans and adapts automatically
1 Part changes
variation, position, geometry
2 Adjust path
in offline programming
3 Download
program to the robot
4 Trial run
check on the cell
↻
Repeated for every change
PART VARIATION
Offline programming: precise, proven, optimised
Autonomous motion: plans and adapts per variant
Overlap: use both together
WHAT IT ADDS
1
Faster start-up for new variants
Path generated from the part model and scan, not taught point by point
2
Fewer trial runs on the cell
Reach, collisions and singularities checked before the robot moves
3
Robust to real-world change
Path corrected to the measured part position during the task
Impact: more variants handled by the same team, and experts focus on process quality
Notes: WHERE AUTONOMOUS MOTION ADDS VALUE (about 60 seconds)
[Point to the scale] This line shows how much the part varies: from the same part every time on the left, to many variants and changing positions on the right.
[Navy bar] On the left, offline programming is the best choice. It is precise, proven and optimised for cycle time.
[Loop in the middle] When the part changes, in its variation, position or geometry, the offline programming workflow follows four steps: we adjust the path, download the program to the robot, and run a trial on the cell. And this cycle is repeated for every change.
[Teal bar] So as variation grows, this cycle repeats more and more often. This is where autonomous motion adds value, because it plans and adapts the path for each variant. In the middle the two overlap, and we use them together.
[Value panel] Autonomous motion adds three things:
1. Faster start-up for new variants: the path is generated from the part model and the scan, instead of being taught point by point.
2. Fewer trial runs on the cell: reach, collisions and singularities are checked before the robot moves.
3. Robustness to real-world change: the path is corrected to the measured part position during the task.
[Impact] The result: the same team can handle more variants, and our experts can focus on process quality instead of repeated path preparation.
So the message is: choose the right level of autonomy for each task.
IF ASKED "Why not just use offline programming?": For stable, high-volume parts, I would. Autonomy makes sense where variation, uncertainty in part position, or the number of variants make repeated programming costly.
IF ASKED FOR NUMBERS: give a real example from your projects (e.g. preparation time for a new variant before vs after), or say measurement is part of the next validation step.